VIRIDIAN SUNERGY

Glass shall be Viridian Sunergy			 * thick, 	+	 		 (Annealed, Heat Strengthened, Toughened and/or Laminated. Please nominate in this section your requirements.)

Sunergy provides advanced energy efficiencies in the control of both solar heat gain and thermal insulation.

* Glass Thicknesses available:

-  Annealed Glass: 4mm, 6mm 8mm or 10mm

- Toughened or Heat Strengthened: 4mm 6mm 8mm or 10mm

- Laminated Glass: 6.38mm, 8.38mm, 10.38mm or 12.38mm

+ Select from the following standard Sunergy colours – Clear, Green, Azur, (monolithic & laminated) Light Green, Bronze, Blue, or Grey (laminated only)

The glass shall comply with the following performance criteria:

| Visible Light Transmission % | U Value | Shading Co-efficient (SC) | Solar Heat Gain Coefficient (SHGC) |
| --- | --- | --- | --- |

Solar control glass may be subject to thermal stress and should therefore be thermally assessed prior to installation.

Heat Soaking - All toughened glass products must be heat soak tested.

Heat soak testing is a destructive test, which reduces the likelihood of spontaneous breakage by converting impurities such as nickel sulphide inclusions.

Heat Strengthening -All glass which requires extra strength and thermal resistance will be heat strengthened. Heat strengthening increases the strength of annealed glass; however it is not a substitute for toughened glass.

In the event of fracturing heat strengthened glass will crack and tends to remain in glazed position.

All glass is to be selected and installed in accordance but not exclusively with the following Australian and/or New Zealand Standards

- AS 1288 Glass in Buildings Selection and Installation

- AS 1170 Minimum Wind Loads on Structures

- AS/NZ 2208 Safety Glazing Materials in Buildings

- AS/NZ 4666 Insulating Glass Units

- AS/NZ 4667 Quality Requirements for cut-to-size and Processed Glass